## Slide 1: First experiments on electron density and plasma position control using X-mode real-time reflectometry, conducted on the WEST tokamak
Maylis Carrard, 3rd year PhD student
R. Sabot, Y. Moudden, R. Nouailletas, E. Lerche, and the WEST team
EPS Plasma Physics, June 29th – July 3rd of 2026

## Slide 2: Outline
Real-time X-mode reflectometry measurements for control
Density and position control experiments
Application to ICRH coupling optimization
Perspectives

## Slide 3: Real-time reflectometry measurements
Reflectometry: radar principle to compute the density profile
Used for physics studies, two polarizations
X-mode real-time measurements
Existing edge reflectometer
New acquisition system and reconstruction algorithm
2ms time step [Carrard, PPCF 2025]
Real-time measurements for plasma control
F. Clairet, RSI, 2010.
C. Bouchand IEEE TNS, 2024
Reflectometry for plasma control
Compact and flexible, suitable for reactor environment: planned for control in future devices (DEMO)
O-mode: Proof-of-concept [Santos, NF 2012], but requires external information on plasma position
X-mode: Interesting because it provides absolute plasma position

## Slide 4: Control inputs from the real-time profiles
Requirements for the control inputs:
Measurement delay: the data processing must be fast enough; the delay from real-time averaging must be low
Measurement reliability: the noise must be low; the quantity must reflect the desired plasma behavior.
: measures the density at an absolute radius
: measures the external radial position of the plasma
: measures the density at a relative radius
(R=cte)
R()
:
Flat region: less noise, but behavior close to the core
Gradient region: behavior of the edge ( control) but more noise
:
Gradient region: less noise
Very edge: more noise, not able to control
Balance between reliability and delay to extract useful information for specific control experiments

## Slide 5: Reflectometry for control on WEST
Plasma Control System (PCS): drives the plasma discharge depending on scenario reference
Sensors (real-time diagnostics, real-time reconstruction) provide information about the plasma state
Actuators act on the plasma following the PCS requests
WEST Plasma Control System
Reference
Actuators
Sensors
Density control: Interferometry sensor ; Gas injection actuator ; Timescale ~ 40ms
Position control: magnetic reconstruction sensor ; PF coils actuators ; Timescale ~ 3ms
Novelty of this work: Use the reflectometry measurements as sensors
Edge density control validated with still plasma

## Slide 6: Outline
Real-time X-mode reflectometry measurements for control
Density and position control experiments
Application to ICRH coupling optimization
Perspectives

## Slide 7: Absolute density control with plasma translation
Absolute density control at during the translation
Control of edge density at a fixed position
Application for RF heating coupling, to move plasma without changing density in front of antennas
Overall density increases
Steepening of the gradient
Plasma translation
Plasma translation of 1 cm inward

## Slide 8: Steepening of the profile under edge density control
Plasma translation of 1 cm
Increase of the core density
Sinusoidal modulation of the radial position at 1Hz with a 4 cm amplitude
Quasi-rigid displacement at the time step of the diagnostics
Steepening of the profile under plasma translation and absolute density control
With edge density control
Standard interferometry control

## Slide 9: Plasma position control
control at
First experiment:
Unstable position control (huge oscillation on the measurements)
Issue: 50 ms delay between magnetic and reflectometry measurement
Solution: Reach the standard magnetics measurement delay of 3 ms (optimize data processing/transfer and reduce delay induced by the averaging)
Second experiment:
Stable control (more noise because reduction of the averaging number)
Validation of plasma position control with X-mode reflectometry

## Slide 10: Outline
Real-time X-mode reflectometry measurements for control
Density and position control experiments
Application to ICRH coupling optimization
Perspectives

## Slide 11: ICRH coupling optimization via the cutoff density
ICRH coupling depends on the distance between and the ICRH antennas
#64053: Density control close to the core: less noise, but less efficient
#64055: Density control close to the edge: more noise but more efficient for coupling
Preliminary results: Positive effect on the ICRH coupling.
Hence, improvement of plasma response and control strategy:
Adjust the plasma scenario to increase the sensitivity of the coupling to the edge density – Local valve instead of top valve
Improve signal properties and tune the controller

## Slide 12: Outline
Real-time X-mode reflectometry measurements for control
Density and position control experiments
Application to ICRH coupling optimization
Perspectives

## Slide 13: Conclusions and perspectives
Conclusions:
Development of real-time X-mode reflectometry measurements
Validation of density and position control with X-mode
Encouraging results on ICRH coupling control
Upcoming experiments:
ICRH/LH coupling optimization (experiment in progress)
Density control with pellets (strong gradient; profile reliability )
Density gradient control with pellets for the core and the gas puff for the edge
Further development:
Interferometry fringe jump correction
Control with multi-diagnostics profile reconstruction
Use in multi-diagnostics fast events detection: LH transition, MHD mode, ELMs…
Control the density gradient to optimize edge transport

## Slide 14: Thank you
Maylis Carrard, 3rd year PhD student
R. Sabot, Y. Moudden, R. Nouailletas, E. Lerche, and the WEST team
EPS Plasma Physics, June 29th – July 3rd of 2026

## Slide 15: Real-time magnetic field
5
4
3
2
0.2
0.1
0
-0.1
-0.2
Toroidal field:
Normalized reference , real-time data
Radius (m)
Radius (m)
Magnetic field(T)
Poloidal magnetic field, shot 59920, tps=39s
Magnetic field(T)
Toroidal magnetic field, shot 59920, tps=39s
Total magnetic field, shot 59920, tps=39s
Magnetic field(T)
5
4
3
2
Radius (m)
Poloidal field:
Real-time data , , a and approximated equation

## Slide 17: Choice of the sensors
ne
R

## Slide 18: Choice of the sensors
: measures the density at a fixed distance to separatrix

## Slide 19: Density vs position control stability
Reflectometer
WEST Plasma Control System
Local density
Plasma position
Density control
Position control
Line integrated density
Plasma position
Gas injection
PF coils
Interferometry
Magnetic reconstruction
>50ms →3ms
3 ms
~40 ms
35 ms

## Slide 20: Control validation experiments
Experiments | Plasma position | Density control sensor | Plasma position sensor
Density control | Still plasma | Reflectometry | Magnetic reconstruction
Density control at a translating position | Translating plasma | Reflectometry ) | Magnetic reconstruction
Density control at absolute position | Translating plasma | Reflectometry | Magnetic reconstruction
Position control | Translating plasma | Reflectometry | Reflectometry
Experiments | Plasma position | Density control sensor | Plasma position sensor
Density control | Still plasma |  | Magnetic reconstruction
Density control at a translating position | Translating plasma |  | Magnetic reconstruction
Density control at absolute position | Translating plasma |  | Magnetic reconstruction
Position control | Translating plasma |  | 
Specific to X-mode reflectometry

## Slide 21: Validation of density control
Density sensor: from reflectometry profile
Application as a back-up for interferometry or correction of fringe jump
Density control with reflectometry

## Slide 22: Steepening of the profile with the plasma translation
Plasma translation of 1 cm
Increase in the profile gradient
Hypothesis of quasi-rigid plasma displacement
Sinusoidal modulation of the LCFS position at 1Hz with a 4 cm amplitude
Quasi-rigid displacement at the time step of the diagnostics (1ms)
Steepening under plasma translation and absolute density control

## Slide 23: Plasma position control
control with
Density control with
Oscillations in the plasma position: control unstable
Delay of 50 ms between magnetic and reflectometry measurement
Reference delay of a few ms for magnetic measurements
WEST PCS
Position reference
PF coils
Reflectometry position
> 50 ms

## Slide 24: Validation of plasma position control
Work on the data processing. Find a balance between:
Delay reduction (less data filtering, less delay induced by the filters)
Measurement reliability (More noise)
Reach the standard magnetics measurement delay of a few ms
Validation of plasma position control with X-mode reflectometry

## Slide 25: Implementation of the O-mode
Real-time adaptation of O-mode to probe further. X-mode only probes until
Inversion issue is direct for O-mode : no influence from the magnetic field. The time delay is directly accessible with a small approximation.
Link the V band from the standard reflectometer. Add the processing to the real-time PC.

## Slide 26: O-mode noisy signals
However, signal noise is very important (maybe due to low gradient ?)
Signal processing (filters) VS processed measurements latency
Part of the process was parallelized to satisfy a 1 ms update time
How to process the signal without increasing the latency?
So signal processing needs to be adapted. Eventually, put safety conditions, interpolation, and weight on the O or X modes.

## Slide 27: Dependance between RF coupling and critical density position
ICRH coupling varies as the inverse of
Reflectometry provides the radial position of a fixed density -> can control
Sensors of reflectometry :
ICRH
antennas
Reflectometry
measurements
varies with , and Erog.
Objectives: Control the coupling by controlling during variations of these three parameters.

## Slide 28: Edge density control for ICRH coupling optimization

## Slide 29: Gradient density control
RT Gradient measurement:
Measurement of edge density profile by reflectometry
Measurement of integrated density by interferometry
Leads to a measurement of the centrale density and the averaged core gradient: real-time value to exploit for gradient control
Gradient control:
Gas injection to control total density
Pellet injection to control central density
Pellet injection
Gas puff
Central interferometry line
Edge reflectometry
Dentral density
Density gradient