## Slide 1: Theory-based integrated modelling of impurity transport in tokamaks
PhD research award – 52nd EPS Conference on Plasma Physics
Max Planck Institute for Plasma Physics, Garching, Germany
Daniel Fajardo
Supervised by Clemente Angioni and Hartmut Zohm

## Slide 2: Impurities are critical in the operation of a fusion reactor
Core performance
Power exhaust
Plasma-wall interaction
Radiative losses
Impurity accumulation
Fuel dilution
Impurity seeding

## Slide 3: Impurities are critical in the operation of a fusion reactor
During my PhD:
Develop a theory-based modelling workflow with impurities
Core performance
Power exhaust
Plasma-wall interaction

## Slide 4: Impurities are critical in the operation of a fusion reactor
During my PhD:
Develop a theory-based modelling workflow with impurities
Validation in ASDEX Upgrade, a tokamak with full-W walls
Core performance
Power exhaust
Plasma-wall interaction

## Slide 5: Impurities are critical in the operation of a fusion reactor
During my PhD:
Develop a theory-based modelling workflow with impurities
Validation in ASDEX Upgrade, a tokamak with full-W walls
Predictions of ITER plasmas
Core performance
Power exhaust
Plasma-wall interaction
Confidence on extrapolation

## Slide 6: Impurities are critical in the operation of a fusion reactor
During my PhD:
Develop a theory-based modelling workflow with impurities
Validation in ASDEX Upgrade, a tokamak with full-W walls
Predictions of ITER plasmas
Core performance
Power exhaust
Plasma-wall interaction
Transport regime might not be the same

## Slide 7: A happy coincidence for my PhD
Develop workflow
Start: Oct. 2021
Finish: Oct. 2024
Validation in AUG
Applications to ITER

## Slide 8: A happy coincidence for my PhD
Develop workflow
Start: Oct. 2021
Finish: Oct. 2024
Validation in AUG
Applications to ITER
ITER announces transition to full-W walls
Oct. 2023
A. Loarte 2023 ITER press release
2024 EPS conference
2025 PPCF 67 065023

## Slide 9
Theory-based modelling workflow

## Slide 10: A little impurity transport theory
convection
diffusion
inward pinch
temperature screening
Neoclassical flux components strongly depend on charge, collisionality and rotation
convection
diffusion
thermo-diffusion
roto-diffusion
pure pinch
Turbulent flux components do not scale strongly with charge or mass
can lead to central accumulation
does not cause strong peaking

## Slide 11: Extended neoclassical model for rotation effects at all collisionalities
Rotation can increase high-Z neoclassical transport by more than an order of magnitude
It can also modify or even reverse the screening coefficient
less TS
more TS
collisionality
no temperature screening
Mach number (rotation)
Hw / Kw from NEO

## Slide 12: Extended neoclassical model for rotation effects at all collisionalities
Rotation can increase high-Z neoclassical transport by more than an order of magnitude
It can also modify or even reverse the screening coefficient
The FACIT model1 was extended2 to include rotation effects at all collisionalities, matching NEO3 drift-kinetic results
1 Maget 2020 PPCF 62 105001
2 Fajardo 2023 PPCF 65 035021
3 Belli 2009 PPCF 51075081
AUG #38910
less TS
more TS
collisionality
no temperature screening
Mach number (rotation)
Hw / Kw from NEO

## Slide 13: Modelling workflow with impurities
ASTRA
core
edge
Profile evolution
STRAHL3
Impurity densities & radiation
FACIT1,2
Neoclassical transport
TGLF-SAT24
Turbulent transport
1 Maget 2020 PPCF 62 105001
2 Fajardo 2023 PPCF 65 035021
3 Dux 2006 IPP report
4 Staebler 2022 NF 61 116007

## Slide 14: Modelling workflow with impurities
Validated on
AUG L-modes5
AUG H-modes6,7
JET-ILW and Alcator C-Mod7
scenario to be modelled is summarized in this box
1 Maget 2020 PPCF 62 105001
2 Fajardo 2023 PPCF 65 035021
3 Dux 2006 IPP report
4 Staebler 2022 NF 61 116007
5 Fajardo 2024 NF 64 046021
6 Fajardo 2024 NF 64 104001
7 Fajardo 2026 NF 66 046005
ASTRA
core
edge
Profile evolution
STRAHL3
Impurity densities & radiation
FACIT1,2
Neoclassical transport
TGLF-SAT24
Turbulent transport

## Slide 15
Full-radius modelling of AUG L-mode plasmas

## Slide 16: Full-radius modelling of AUG Ar seeded radiative L-mode
Experiment with Paux ~ 7.5 MW but Psep PLH: feedback with Ar seeding1
High Prad / Paux ≈ 70%
H98 ≈ 0.95 without ELMs
AUG 0.8 MA with Ar
1 Fable 2022 NF 62 024001
Simulation of main plasma with three impurities2: Ar, W and B
High confinement is reproduced
Simple model for X-point radiation was included; total radiation matched
Removing argon from the simulation leads to 33% lower confinement
2 Fajardo 2024 NF 64 046021
AUG #37041 at 5.0-5.5 s

## Slide 17
Modelling the control of W accumulation with central ECRH

## Slide 18: Dynamical modelling of AUG H-mode with NBI + ECRH steps
AUG 1.0 MA H-mode
AUG #32408
W accumulation as central ECRH is decreased1
Central wave heating controls W accumulation because it increases W diffusivity and decreases W pinch
1 Angioni 2017 NF 57 056015

## Slide 19: Dynamical modelling of AUG H-mode with NBI + ECRH steps
AUG 1.0 MA H-mode
AUG #32408
W accumulation as central ECRH is decreased1
Central wave heating controls W accumulation because it increases W diffusivity and decreases W pinch
ASTRA-TGLF-FACIT modelling of entire flattop quantitatively reproduces experimental W behavior2
Competition between neoclassical convection and turbulent diffusion
1 Angioni 2017 NF 57 056015
2 Fajardo 2024 NF 64 104001

## Slide 20: Dynamical modelling of AUG H-mode with NBI + ECRH steps
AUG 1.0 MA H-mode
1 Angioni 2017 NF 57 056015
2 Fajardo 2024 NF 64 104001
W accumulation as central ECRH is decreased1
Central wave heating controls W accumulation because it increases W diffusivity and decreases W pinch
ASTRA-TGLF-FACIT modelling of entire flattop quantitatively reproduces experimental W behavior2
Competition between neoclassical convection and turbulent diffusion → different W profiles at different ECRH
AUG #32408

## Slide 21
ITER 15 MA baseline scenario

## Slide 22: Modelling the 15 MA baseline scenario including tungsten
Bt = 5.3 T, 50/50 D-T mix
Boundary condition at pedestal top
Pedestal calculated with IMEP1
30 MW of NBI
Scan in ECRH power: 0, 10, 20, 50, 70 MW
Scan in pedestal top W concentration: 10-5 to 10-4
ITER 15 MA H-mode in DT
1 Luda 2025 NF 65 072001

## Slide 23: W profile shape & radiation are independent of ECRH power
W density profile shape is practically not affected by ECRH1
As a consequence, the radiated power losses are also independent of ECRH
ITER 15 MA H-mode in DT
1 Fajardo 2024 NF 64 104001
ITER 15 MA

## Slide 24: W profile shape & radiation are independent of ECRH power
W density profile shape is practically not affected by ECRH1
As a consequence, the radiated power losses are also independent of ECRH
ITER 15 MA H-mode in DT
1 Fajardo 2024 NF 64 104001
AUG #32408
ITER 15 MA

## Slide 25: Turbulent transport is dominant for W in ITER core
In the core of ITER, the much lower collisionality and lower rotation (compared to present-day devices) cause the neoclassical transport to be almost negligible compared to turbulent transport
Turbulent transport does not lead to strong accumulation1
Core W densities are flat regardless of ECRH power2
1 Angioni 2021 PPCF 63 073001
2 Fajardo 2024 NF 64 104001
AUG 1.0 MA H-mode
(+ 8 MW of NBI)
ITER 15 MA H-mode
(+ 30 MW of NBI)

## Slide 26: Operational limits by W are given by H-mode sustainment
ITER 15 MA H-mode in DT
Global condition of Psep PLH is reached before the central power balance is negative locally1
Depending on the W content, auxiliary heating must be adjusted to offset global radiative losses
The W concentration limited by H-mode sustainment: at PECRH = 20 MW
1 Fajardo 2024 NF 64 104001

## Slide 27: Interplay between plasma performance, heating and W content
ITER 15 MA H-mode in DT
ITER targets are satisfied, as long as is low enough2
Auxiliary heating can be raised to tolerate more W (lower Q) or lowered to reach higher Q
Little sensitivity of pedestal pressure to ECRH power in ITER1 and stiff core profiles
1 Luda 2025 NF 65 072001
2 Fajardo 2025 PPCF 67 015020
(+ 30 MW of NBI)

## Slide 28
Full-radius modelling of the current ramp-up in ITER

## Slide 29: ITER current ramp-up simulations
ITER L-mode ramp-up in D
5.0
6.0
7.5
9.0
10.0
11.5
20.0
40.0
70.0
2.0
2.2
2.5
2.8
3.0
3.3
5.0
9.0
15.0
1 Loarte 2025 PPCF 67 065023
2 Fajardo 2025 PPCF 67 015020
New ITER full-W wall brings particular interest to limiter phase1
Dynamical modelling of limiter to diverted plasmas during Ip ramp over 65 seconds
Full-radius L-mode simulations, motivated by previous modelling of ITER electron-heated L-modes2
Scan W source to assess limits on W concentration

## Slide 30: Limits of W content for plasma survival
W concentration during limiter phase of 10-4 is tolerable, 3×10-4 is problematic1
Plasma marginally survives at highest W source, but edge Te collapses and W pedestal develops
ITER L-mode ramp-up in D
1 Fajardo 2025 PPCF 67 015020
without W
intermediate W
maximum W
maximum W source, profiles before EC step

## Slide 31: Slightly modified ECRH ramp alleviates problems at high W
Optimized heating trajectory avoids transient increase of W radiation at high W source
Higher W concentrations can be tolerated by slightly modifying the ECRH ramp1
ITER L-mode ramp-up in D
1 Fajardo 2025 PPCF 67 015020
without W
intermediate W
maximum W with faster ECRH ramp
maximum W source, profiles before EC step

## Slide 32
Summary and conclusions

## Slide 33: Key takeaway points
for W: frot ≈
(1 + (8 Mi)2 )2
1 + (8 Mi)4 / 50
Theory-based integrated modelling with impurity transport → validated on present experiments → allows quantitative predictions
Transition from dominant neoclassical to turbulent W transport towards reactors
In ITER, auxiliary heating power is required to keep the plasma in H-mode, not to control central W accumulation
Predictive modelling allows optimization of heating trajectories in transient phases like current ramps
More neoclassical: potential for accumulation
More turbulent: flat core high-Z densities
Notes: Integration challenge of radiated power-dilution-confinement
Future simulation of rotation

## Slide 34: Key takeaway points
3 Muraca 2026 PPCF
3
1,2
Theory-based integrated modelling with impurity transport → validated on present experiments → allows quantitative predictions
Transition from dominant neoclassical to turbulent W transport towards reactors
In ITER, auxiliary heating power is required to keep the plasma in H-mode, not to control central W accumulation
Predictive modelling allows optimization of heating trajectories in transient phases like current ramps
2 Perks 2025 PoP
for W: frot ≈
(1 + (8 Mi)2 )2
1 + (8 Mi)4 / 50
More neoclassical: potential for accumulation
More turbulent: flat core high-Z densities
¡Vamos Colombia!
1
1
1 Fajardo 2026 NF
Notes: Integration challenge of radiated power-dilution-confinement
Future simulation of rotation

## Slide 35
Additional material

## Slide 36: Simulations of ECRH-only AUG H-modes
AUG H-modes with only ECRH
AUG #37909
Database of 12 AUG H-modes spanning PECRH {0.7 – 4.3} MW, Ip {0.6 – 1.2} MA, ne {1.9 –8.4} 1019 m-3
Overall flat W profiles: low intrinsic rotation
Better confinement prediction than scalings
[Fajardo 2026 NF 66 046005]

## Slide 37: Full-radius modelling of JET high power Ne seeded plasmas
High current Ip = 3.2 MA at Bt = 3.45 T (q95 ~ 3.3) in deuterium
28 MW of NBI, 4 MW of ICRH
Neon seeding: low, intermediate, high
[Giroud 2025 IAEA FEC]
JET-ILW 3.2 MA 32 MW with Ne

## Slide 38: Full-radius modelling of JET high power Ne seeded plasmas
High current Ip = 3.2 MA at Bt = 3.45 T (q95 ~ 3.3) in deuterium
28 MW of NBI, 4 MW of ICRH
Neon seeding: low, intermediate, high
[Giroud 2025 IAEA FEC]
Including neon is necessary to reproduce the main profiles and global confinement in the simulations
JET-ILW 3.2 MA 32 MW with Ne
1 Fajardo 2026 NF 66 046005
Flat radiation profiles by W and Ne
Excellent agreement with experiment across all transport channels1

## Slide 39: Simulations of Alcator C-Mod plasmas with Molybdenum
C-Mod H-,I- & L-modes in D
I-mode
H-mode
[Fajardo 2026 NF 66 046005]

## Slide 40: Full-radius simulations of electron-heated ITER L-modes
ITER 5 & 7.5 MA L-modes in D
5.0 MA with 20 MW and 40 MW of ECRH
7.5 MA with 40 MW of ECRH
Bt = 2.65 T, D plasmas, constant GW fraction
[Fajardo 2025 PPCF 67 015020]

## Slide 41: Radiation and access to H-mode
With our modelling assumptions, 20 MW of ECRH do not allow access to H-mode
40 MW of ECRH enables H-mode operation in D provided the separatrix W concentration remains below: 3×10-4 at 5MA, 1.5×10-4 at 7.5MA
ITER 5 & 7.5 MA L-modes in D
7.5 MA, 40 MW
5.0 MA, 40 MW
5.0 MA, 20 MW
[Fajardo 2025 PPCF 67 015020]

## Slide 42: Main plasma profiles
ITER 15 MA H-mode in DT
Pedestal calculated with IMEP1, kept fixed across the scans in ECRH power and W concentration
Core profiles evolved using TGLF-SAT2
Rotation profile from previous predictions2,3 was kept fixed, fusion power might be sensitive to it1
TGLF-SAT2 + IMEP
1 Luda 2025 NF 65 072001
2 Singh 2017 NJP 19 055004
3 Chrystal 2020 NF 60 036003

## Slide 43: Interplay between plasma performance, heating and W content
Pedestal top pressure at IMEP (& EPED) value of 130 kPa gives:
        better performance in Q (+1-5 w.r.t. 108 kPa)1
        Higher margin for H-mode sustainment due to higher alpha heating (+20-30MW w.r.t. 108 kPa)1
ITER 15 MA H-mode in DT
ITER targets are satisfied, as long as and PLH are low enough
Auxiliary heating can be raised to tolerate more W (lower Q) or lowered to reach higher Q
Little sensitivity of pedestal pressure to ECRH power in ITER2
1 Fajardo 2025 PPCF 67 015020
2 Luda 2025 NF 65 072001
x → H-mode not sustained
(+ 30 MW of NBI)

## Slide 44: Transition from dominant neoclassical to turbulent W transport
In present-day devices, core W convection is mostly neoclassical and diffusion is mostly turbulent
In reactor core, much lower collisionality (and rotation) → convection is also mostly turbulent
calculated with transport codes
Simple rule-of-thumb with known/expected plasma parameters
for tungsten: frot ≈
(1 + (8 Mi)2 )2
1 + (8 Mi)4 / 50

## Slide 45: Transition from dominant neoclassical to turbulent W transport
In present-day devices, core W convection is mostly neoclassical and diffusion is mostly turbulent
In reactor core, much lower collisionality (and rotation) → convection is also mostly turbulent
More neoclassical: potential for accumulation
More turbulent: flat core high-Z densities
for tungsten: frot ≈
(1 + (8 Mi)2 )2
1 + (8 Mi)4 / 50

## Slide 46: Transition from dominant neoclassical to turbulent W transport
In present-day devices, core W convection is mostly neoclassical and diffusion is mostly turbulent
In reactor core, much lower collisionality (and rotation) → convection is also mostly turbulent
3
1,2
1
1 Fajardo subm. to NF
2 Perks subm. to NF
3 Muraca 2025 EU-US TTF
1
for W: frot ≈
(1 + (8 Mi)2 )2
1 + (8 Mi)4 / 50