## Slide 1: PENKNIFE
Plasma Edge Numerics using
Kinetic Neutrals Integrated in Finite Elements
James Edgeley and UKAEA edge code team

## Slide 2: PENKNIFE
Mean Field Transport
Multiple species
Closure options
Kinetic neutral reactions
VANTAGE coupled
Electrostatic turbulence
Nektar++ meshing support
2D, Axisymmetric or full 3D geometry
Implicit, non-linear solver
Reduced Braginskii equations
Sheath boundary conditions
Flexible B field configuration
Working towards full performance portability
Anomalous diffusion

## Slide 3
VANTAGE
NESO
PENKNIFE
NESO Library
Reactions
Boundary Conditions
Surface Reactions
Ionisation
CX
Recombination
ReactionSystem
Sources/sinks
Evaluation
Projection
Source deposition
Merge/removal
Integrators
Closures
Riemann Solvers
Magnetic field control
PlasmaSystem
Anistropic diffusion
Reduced Braginskii
Electrostatic Turbulence

## Slide 4: Drifts and spurious currents

## Slide 5: Reduced Equations

## Slide 6: Reduced Braginskii equations
No particle sources
Braginskii closure for heat flux and collisional heating
Anomalous diffusion
Advection, diffusion and forcing working as expected

## Slide 7
Evolve and perform elliptic solve for
2D Tilted driftwave shows zonal flow.
Insufficiently resolved for smallest vortices
Add small amount of diffusion to vorticity equation
But there’s a problem when currents are added

## Slide 8: Spurious currents
Elliptic solve for in DG gives left and right values for E
Small spurious currents flowing into or out of boundary nodes
Curved elements
Elliptic vector potential solve
Riemann solver (average)

## Slide 9: Axisymmetry and code comparison

## Slide 10: Neutral movement in axisymmetric geometry
Neutrals move in straight lines in 3D, but particles are constrained to 2D mesh
How to represent 3D neutral paths without introducing extra dimension.
Include fictitious force in particle pusher.
Verlet/leapfrog integration leads to energy drift
Conservation requires different approach

## Slide 11: VANTAGE coupling
Thermal neutral source at outer midplane
Ionisation on fixed plasma background
Convergence to steady-state
Single mesh, multiple domains

## Slide 12: EIRENE comparison
Ionisation and wall pumping
Steady state reached after around 50ms
Integral of ionisation source reaches to 3.08e19/s vs EIRENE 3.75e19/s
5e21/s source. Absorption at wall set too high (10%)
Thermal source of neutrals at OMP
Neutral advection only – excellent agreement with EIRENE – with less noise

## Slide 13: Marker particles and FEM reconstruction

## Slide 14: Recombination and marker particles
VANTAGE requires marker particle sources for the recombination reaction.
Random distribution to avoid bias, but is not consistent with FEM integration
Marker particles’ weight must be adjusted according to their distribution in the cell before sampling FEM field
FEM field
Evaluation at particle positions
Multiplication by particle "mass"
Particle weight
FEM Projection

## Slide 15: Consistent Marker Weights
Key observation is mass matrix must be consistent from FEM integration points and particle positions
Using
, , ,
Mass matrix equality be written as:
This is easily solved for sufficient rank with a pseudoinverse or minimum norm linear least squares solver (e.g. LAPACK dgelsd)

## Slide 16: Avoiding negative weights
Kinetic model requires all positive weights, whereas FEM has no such restriction
Solving produces a solution with minimum norm relative to 0, therefore some weights are highly likely to be negative.
Instead make a substitution Transforming the matrix equation into:
is the natural weight for each cell
Now the solution weights are clustered around
Can repeat solve until all weights are positive

## Slide 17: Marker weights
Uniform distribution of (static) marker particles.
Particles in voids are assigned higher masses
Particles in clusters are assigned lower masses
2D 200 markers/cell P=3 has ~0.01% error

## Slide 18: Status and outlook

## Slide 19: Status
FEM track
Basic advection-diffusion solver
Field aligned operators
Field aligned operators ∇_∥, ∇_⊥
Kinetic track
Basic coupling to VANTAGE (ionisation/cx/recombination)
Merge, remove and project transformations
Physics track
Multispecies reduced equations
Braginskii closure
Basic surface reactions (absorption/reflection)
Advanced surface reactions (TRIM data/recycling)
Binary reactions and molecular processes
Zhdanov closure
EM turbulence
Electrostatic turbulence and drifts
Improved preconditioning, meshing and GPU execution
Implicit non-linear solver
Improving turbulence numerics
FEM track
Basic advection-diffusion solver
Kinetic track
Basic coupling to VANTAGE (ionisation/cx/recombination)
Merge, remove and project transformations
Physics track
Multispecies reduced equations
Braginskii closure
Basic surface reactions (absorption/reflection)
Advanced surface reactions (TRIM data/recycling)
Binary reactions and molecular processes
Zhdanov closure
EM turbulence
Electrostatic turbulence and drifts
Improved preconditioning, meshing and GPU execution
Implicit non-linear solver
Improving turbulence numerics
PENKNIFE capability progressing in parallel and in conjunction with Nektar++ and VANTAGE development

## Slide 20: Future
Keep pace with VANTAGE development
Adopt numerical and meshing techniques from Nektar++ collaboration
Currently have only explored simple geometry for the complex models and simple models for the complex geometry.
SUNRISE will unlock the complex geometry, complex model capability