## Slide 1: GUERNICA: Overcoming Challenges Associated With 2X3V Kinetic Neutrals
Jack Gabriel and Saskia Mordijck
William & Mary
UKAEA Exhaust Code Workshop

## Slide 2: GUERNICA: 2X3V Kinetic Neutral Solver
Equation: Boltzmann for atomic hydrogen on a static background plasma
Configuration space: DG on unstructured quadrilaterals, nodal Gauss–Lobatto basis, upwind flux, matrix-free, built on MFEM
Velocity space: discrete velocity method on a uniform Cartesian grid
Collision operators: Charge exchange, ionization, radiative recombination, conservative BGK neutral-neutral*
Transient
Steady-state

## Slide 3: How Long Does A Code Take To Run?
Wall Clock Time = # of iterations x time per iteration
Part 1: Speeding up charge exchange
Part 2: The negative consequences of the choices made to speed up charge exchange
Part 3: Fixing the negative consequences of the choices made to speed up charge exchange
Part 4: The serendipitous potentially positive consequences of fixing the negative consequences of the choices made to speed up charge exchange

## Slide 4: Cost Per Iteration
Part 1

## Slide 5: Full CX Matches DEGAS2; Meier CX Does Not
Full CX: a convolution in velocity
Velocity-dependent loss, gain from the full integral
Meier approximation: eliminating velocity dependence
Velocity-independent loss rate; new neutrals get the ion Maxwellian
Low-density Bernard benchmark: Ti = 60 eV, n = 5×10¹⁸ m⁻³, L = 40 m, recycling walls (R = 1)
Full CX reproduces DEGAS2 results to within its noise
Meier over-penetrates: Increased temperature profile leads to increased penetration, 31% too many neutrals overall
One code, mesh and velocity grid; only the CX operator swapped

## Slide 6: CX Is Slow; FFT Makes It Fast(er)
Low-density benchmark | Full CX fp64 | Full CX fp32 | Meier (Gkeyll)
CX operator per iteration | 695.6 ms | 103.7 ms | 3.1 ms
Wall time to a 10⁻⁵ residual | 75.9 min | 18.4 min | 8.3 min
FFT brings full CX operator from
FFT at 483 is 1300x faster than direct: 0.55s vs 12 min
90-95% of each iteration is CX for fp64
fp32 is 3.5-7.6x faster than fp64; solution changes by 6x10-7

## Slide 7: The Issue With Uniform Cartesian Grids
Part 2

## Slide 8: Preliminary MAST-U Demonstration
Setup
SOLPS-ITER background, shot 45470 at 0.42 s; ions = electrons
Planar 2D, 709 quads to the first wall, p = 1
108 × 108 × 26 velocities over ±4.7×10⁵ m/s
Recycling walls at 2 eV
Ionization + CX + recombination
Results
4,000 iterations in 86 min on one A5000 with fp32 CX (6.0 h in fp64): 8.6×10⁸ phase-space DOFs, 18.8 of 24 GiB
Particle and energy balance to 3×10⁻⁹
Peak nn = 8×10¹⁷ m⁻³ at the lower inner strike point; Tn from a few eV to > 100 eV

## Slide 9: Consequences Of Under-Resolved Velocity Space
Converged ≠ Correct
MAST-U: ≈ 1.6 points per thermal speed of the 2 eV neutrals, between 16² and 32²
Looks like under-sampled EIRENE, but the cause is discretization, not statistics
Uniform Cartesian grid has major drawbacks
Allows for fast CX evaluation BUT,
One grid for 2 eV wall neutrals and > 100 eV CX neutrals
≈ 1283 points needed: does not fit in GPU memory

## Slide 10: Moving To A Spherical Grid
Part 3 (and some of 4)

## Slide 11: From Uniform Cartesian To Spherical Velocity Space
~7× fewer velocity points: 54 speeds × 12 × 64 directions = 41,472 against ≈ 300,000
CX without the FFT: Legendre expansion of the kernel (L = 8), ~10⁻⁴ accuracy to Mach 6, ~20× fewer operations

## Slide 12: Conclusions
GUERNICA: a 2X3V continuum kinetic neutral solver that keeps the full charge-exchange operator
Reducing cost of charge exchange
  Full CX reproduces DEGAS2; the Meier approximation over-penetrates
  The FFT makes full CX 1300× faster than direct evaluation, and an fp32 convolution a further 3.5–7.6×
  A uniform Cartesian grid allows the FFT but under-resolves the cold wall neutrals: ray effects
Plans to take advantage of a spherical velocity grid
  A log-spaced spherical grid covers 2 eV wall neutrals to the hot core with ~7× fewer points with better accuracy (in development)
  Explicit pseudo-time stepping is limited by stability, so convergence can still be slow
  Advection sweeps invert transport and loss exactly: no stability limit (in development)

## Slide 13: Backup

## Slide 14: Number Of Iterations
Part 3

## Slide 15: From Time Stepping To Advection Sweeps
1. Transient
The origin story
SSP-RK3 with one global step
The fastest velocity in the smallest element sets Δt for every unknown
for MAST-U demonstration
2. Pseudo-time
Today’s steady solver
Forward Euler, local step per element–velocity pair
Still explicit: a transport limit and a collisional limit (νΔτ < 2)
Convergence can still be slow
3. Advection sweep
Moving forward
Per direction, solve elements in downwind order (4 × 4 local system at p = 1)
Transport and loss inverted exactly: no stability limit
Basic idea can be applied for both steady state and transient
Why not fully implicit? Memory constraints!

## Slide 16: Stability And Convergence Of Pseudo-Time Stepping
Largest stable pseudo-time parameter
Iterations to a 10⁻⁶ residual
Two stability limits
Transport: Δτ0 ≤ 0.36, 0.08, 0.035, 0.018 for p = 1–4
Collisional: νΔτ < 2, so Δτ0 < 0.33/ne for every p
Cost of one iteration is independent of collisionality; the number of iterations is not.
Notes: Forward Euler in pseudo-time with a local step per element-velocity pair. Scan in collisionality L/lambda ~ 20 n_e / 1e18 m^-3 from 1 to 1000.
Two stability limits:
- Transport limit (low collisionality): largest stable dtau0 is 0.36, 0.08, 0.035, 0.018 for p = 1, 2, 3, 4. It roughly halves with each order above p = 2.
- Collisional limit (high collisionality): forward Euler needs nu*dtau < 2, giving dtau0 < 0.33/n_e, the same for every p.
Iterations to bring all residuals below 1e-6: about 2,000 / 7,500 / 14,000 / 27,000 for p = 1-4 at low collisionality; the same for every p at high collisionality, growing with density to about 19,500 at L/lambda = 1000.
Consequences: the cost of one iteration does not depend on collisionality, but the number of iterations does. Higher order is more accurate per node but costs more iterations.

## Slide 17: Conclusions
GUERNICA: a 2X3V continuum kinetic neutral solver that keeps the full charge-exchange operator
Reducing cost of charge exchange
  Full CX reproduces DEGAS2; the Meier approximation over-penetrates
  The FFT makes full CX 1300× faster than direct evaluation, and an fp32 convolution a further 3.5–7.6×
  A uniform Cartesian grid allows the FFT but under-resolves the cold wall neutrals: ray effects
Plans to take advantage of a spherical velocity grid
  A log-spaced spherical grid covers 2 eV wall neutrals to the hot core with ~7× fewer points with better accuracy (in development)
  Explicit pseudo-time stepping is limited by stability, so convergence can still be slow
  Advection sweeps invert transport and loss exactly: no stability limit (in development)

## Slide 18: Operator Tests
Ionization decay
SSP-RK3 converges at 3rd order in νΔt
CX rate between two Maxwellians
4th order in Δv (lattice rule, conical kernel singularity)
Wall boundary condition
4th order in the mesh at p = 3
Notes: Verification of the individual pieces.
- Ionization: exponential decay advanced with SSP-RK3; the error in n(t = 2) falls at third order in nu*dt.
- Charge exchange: the discrete CX rate between two Maxwellians converges at 4th order in the velocity spacing, the expected rate for a lattice rule with a conical singularity in the kernel.
- Wall boundary condition: emitting-wall test converges at 4th order in the mesh at p = 3.

## Slide 19: BGK Validation
Relative change in mass, momentum and energy
Kinetic entropy
Conservative: Mieussens discrete equilibrium holds mass, momentum and energy to round-off (2.4×10⁻¹³)
Entropy increases monotonically
Newton solve: O(Nvx + Nvy + Nvz), at most 3 iterations
Cost: about 2% of CX
Transient mode only for now
Notes: Neutral-neutral collisions use a BGK operator with the Mieussens discrete equilibrium, so mass, momentum and energy are conserved at the discrete level.
- Periodic relaxation test with an anisotropic perturbation: conserved quantities stay constant to round-off (2.4e-13), and the kinetic entropy increases monotonically.
- The Newton Jacobian for the equilibrium factorises on the tensor velocity grid, so it costs O(N_vx + N_vy + N_vz) and converges in at most 3 iterations.
- BGK costs about 2% of CX.
- A different pseudo-time step for each velocity breaks this discrete conservation, so BGK currently runs only in transient mode; a moment-preserving pseudo-time update is in progress.

## Slide 20: Computational Cost
Cost vs velocity points
Cost vs number of elements
CX is 90–95% of each iteration in fp64
FFT: scales as Nv1.13; direct as Nv2.02
fp32 convolution: 3.5–7.6× faster
≈ 4.5 ns per phase-space DOF per iteration once the GPU is saturated
Linear in elements, roughly independent of p
Notes: Cost per phase-space degree of freedom per iteration, on one RTX A5000.
- CX is 90-95% of each iteration in double precision; nothing else is worth optimising. BGK costs about 2% of CX.
- The FFT convolution takes 11.5 ms at 16^3 velocities and 1.25 s at 64^3, scaling as N_v^1.13; direct evaluation scales as N_v^2.02.
- Running only the convolution in fp32 is 3.5-7.6x faster and changes the high-density DEGAS2 benchmark solution by 6e-7.
- Once the GPU is saturated the cost is about 4.5 ns per phase-space DOF per iteration in double precision. It is linear in the number of elements and roughly independent of polynomial order.

## Slide 21: Spatial And Velocity Convergence
DG error vs number of elements
Error vs velocity points, even and odd N
Space: O(Δxp+1) for p = 1–4, also on randomly perturbed meshes
Velocity, even N: exponential convergence down to the DG error
Velocity, odd N: composite Simpson weights converge at half the rate
Notes: Spatial: the DG discretisation converges at the expected O(dx^(p+1)) for p = 1-4, including on randomly perturbed meshes.
Velocity: the even-N rule is the "alternative extended Simpson" rule (trapezoid rule with fourth-order end corrections) and converges exponentially once the distribution has decayed at the grid edges. Odd N uses composite Simpson weights, which alternate and converge at half the exponential rate. Both level off at the DG error.
History: the code only accepted odd N until late August, which is why earlier MAST-U runs used N_vz = 25. An even-vs-odd comparison at N_vz ~ 25 changed energy quantities by about 14%, because neither resolves the 2 eV Maxwellian.

## Slide 22: MAST-U Demonstration: Background And Mesh
Plasma density
Plasma temperature
GUERNICA mesh
SOLPS-ITER background, shot 45470 at 0.42 s: ohmic L-mode, double null, conventional divertor
Ion fields set equal to the electron fields
Planar 2D, uniform toroidally
709 quadrilaterals out to the first wall, p = 1
108 × 108 × 26 velocities over ±4.7×10⁵ m/s
Recycling walls at 2 eV; ionization + CX + recombination
Notes: Background plasma from a SOLPS-ITER simulation of MAST-U shot 45470 at 0.42 s: ohmic L-mode, double null, conventional divertor (Moulton et al., Nucl. Fusion 64, 076049, 2024). Ion fields are set equal to the electron fields.
Planar 2D cross-section, uniform toroidally (no cylindrical geometry terms). 709 quadrilaterals from Gmsh extending to the first wall, p = 1.
Velocity grid 108 x 108 x 26 over +/-4.7e5 m/s. Recycling walls at 2 eV. Ionization, CX and recombination on. fp32 CX.

## Slide 23: MAST-U Demonstration: Neutral Solution
Neutral density
Neutral flux
Neutral temperature
Peak nn = 8×10¹⁷ m⁻³ at the lower inner strike point
Tn from a few eV in the divertor chambers to > 100 eV in the core
Flux streamlines run from the strike points to the walls
Faint streaks from the strike points are ray effects
Notes: Steady-state neutral solution.
- Peak neutral density 8e17 m^-3 at the lower inner strike point.
- Neutral temperature goes from a few eV in the divertor chambers to above 100 eV in the core.
- Streamlines of the neutral flux run from the strike points through the domain to the walls.
- Faint streaks from the strike points follow the velocity-grid directions: ray effects, with about 1.6 velocity points per thermal speed of the 2 eV recycled neutrals.

## Slide 24: MAST-U Demonstration: Balance And Convergence
Residuals, fp32 (solid) and fp64 (dashed)
Ionization removes 18% of emitted neutrals; 82% are absorbed at the walls
Balances close to 3×10⁻⁹ relative
fp32: residual floor 5×10⁻⁷ to 8×10⁻⁶
fp64: residuals reach 4×10⁻¹⁴ – 10⁻¹²; density changes by 2×10⁻⁷
4,000 iterations: 86 min in fp32, 6.0 h in fp64
Notes: Global particle and energy balance, and residual convergence.
- Ionization removes 18% of the emitted neutrals; the other 82% are absorbed at the walls.
- Particle and energy balances close to 3e-9 relative.
- 4,000 iterations: 86 min with the fp32 convolution, 6.0 h in double precision, for 8.6e8 phase-space DOFs and 18.8 of 24 GiB.
- Residuals drop about 8 orders of magnitude, then level off at the fp32 floor (5e-7 to 8e-6). In fp64 they continue to 4e-14 to 1e-12, and the density changes by only 2e-7.
- CX particle non-conservation is 4e-8 of the wall emission in fp32 against 3e-16 in fp64.

## Slide 25: MAST-U Demonstration: Reaction Rates
Particle rates: recombination, ionization, charge exchange
Energy rates: recombination, ionization, charge exchange
Ionization is the main volumetric sink of neutral particles and energy
Charge exchange conserves particles (Rcx at round-off); in energy it is a source inside the plasma and a sink near the walls
Recombination is a small source; radiative only, three-body still to be added
Notes: Steady-state particle (R) and energy (P) exchange rates for recombination, ionization and charge exchange. Red is a source for the neutrals, blue a sink.
- Ionization is the main volumetric sink of neutral particles and energy.
- Charge exchange conserves particles, so R_cx is at round-off (non-conservation is 4e-8 of the wall emission with the fp32 convolution). In energy it is a source for neutrals inside the plasma and a sink near the walls.
- Recombination is a small source. Only radiative recombination is included; three-body recombination is still to be added.

## Slide 26: Fundamental Tradeoff Of Modeling
Speed
Accuracy
vs.
How can we get 2X3V kinetic neutrals fast without compromising accuracy?