## Slide 1
KN1DPy: A Python translation of KN1D
UKAEA Exhaust Code Workshop 2026
Jamie Dunsmore
MIT PSFC
Jerry Hughes
Aaron Ho
Brian LaBombard
Steven Thomas
William & Mary
Nicholas Brown
Saskia Mordijck
IPP CAS
Daniel Švorc

## Slide 2
Outline
Introduction to KN1D
The Python translation and kn1d-lite
Recent applications of KN1D
Comparisons against 2D codes
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 3
Outline
Introduction to KN1D
The Python translation and kn1d-lite
Recent applications of KN1D
Comparisons against 2D codes
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 4
KN1D: Kinetic Neutrals in 1-Dimension
KN1D is a kinetic neutrals code with 1 spatial dimension and 2 velocity dimensions. It solves for the fH and fH2 distribution functions on a plasma background.
Originally written (in IDL) by B. LaBombard in 2001 for fuelling studies on Alcator C-Mod
Smick et al. Nuclear Fusion (2013)
Han et al. Nuclear Fusion (2023)
Luda et al. Nuclear Fusion (2024)
IMEP modelling framework on AUG
Cross-field particle transport on TCV
Scrape-off-Layer flows on Alcator C-Mod
Hughes et al. Physics of Plasmas (2006)
Pedestal fuelling on C-Mod
KN1D is fast (~10s per run) and kinetic, but uses a simplified 1D slab geometry
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 5
The code uses 1D slab geometry, with neutrals born from the limiter sides
Scalar Inputs
PH2: molecular pressure at the gauge
Isotope mass
Profile Inputs (defined on x)
ne
Te
Ti
Lc (connection length)
vx (plasma velocity profile)
Outputs
fH (x, vx, vr)
fH2 (x, vx, vr)
Derived quantities
x=0
xlim
xsep
x
Lc
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 6
x=0
xlim
xsep
x
H2
H
H+
The code uses 1D slab geometry, with neutrals born from the limiter sides
Scalar Inputs
PH2: molecular pressure at the gauge
Isotope mass
Profile Inputs (defined on x)
ne
Te
Ti
Lc (connection length)
vx (plasma velocity profile)
Outputs
fH (x, vx, vr)
fH2 (x, vx, vr)
Derived quantities
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 7
KN1D solves the Boltzmann equation for fH and fH2 using the method of successive generations
Molecules
Source from pressure gauge and limiter recycling of atoms and plasma
Sink from all collisional processes (dissociation, elastic scattering etc.)
Recycling source from previous generation
Charge-exchange source from previous generation
Sink from all collisional processes
Elastic scattering source from previous generation
0th generation
jth generation
Same procedure is used to solve for the atoms (although precise sources and sinks are slightly different)
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 8
Outline
Introduction to KN1D
The Python translation and kn1d-lite
Recent applications of KN1D
Comparisons against 2D codes
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 9
KN1DPy matches the IDL results for test cases on C-Mod, DIII-D and MAST-U (N. Brown)
Code improvements in Python version:
Important inputs like the velocity/spatial mesh resolution and different collision toggles can now be specified in a config file
Straightforward to add new rate coefficients into the code
Includes a reduced version of KN1D that runs from the separatrix inwards: kn1d-lite
https://github.com/W-M-plasma-group/KN1DPy
Max error between Python and IDL neutral profiles: <0.1%
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 10
kn1d-lite solves for the atomic neutrals inside the separatrix
x=0
xlim
xsep
x
H2
H
H+
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 11
x=0
x
H
H+
Idea
Specify plasma profiles inside the LCFS and the n0 distribution function at the LCFS
Removes complexity/uncertainty surrounding recycling model, treatment of molecules and plasma profiles in the SOL
Runs in a couple of seconds
kn1d-lite solves for the atomic neutrals inside the separatrix
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 12
Outline
Introduction to KN1D
The Python translation and kn1d-lite
Recent applications of KN1D
Comparisons against 2D codes
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 13
Application 1: kn1d-lite to supply Sion in reduced models for the density pedestal
Saarelma-Connor model couples a reduced plasma transport model to a two-jet neutral model in the pedestal
Saarelma et al. Nuclear Fusion (2023)
Saarelma et al. Nuclear Fusion (2024)
Model assumes negligible edge ionisation source at 𝜓N = 0.85, but validation on DIII-D shows that this is not the case with the two-jet model
Dunsmore et al. In preparation (2026)
Using KN1D as the neutrals model improves agreement with experimental ne profiles
kn1d-lite
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 14
Application 2: kn1d-lite as the neutrals model in TORAX (A. Ho)
kn1d-lite
Work still ongoing, but agreement has improved by including kn1d-lite and sawteeth (ST) in the model.
C-Mod Ohmic L-mode test case
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 15
Outline
Introduction to KN1D
The Python translation and kn1d-lite
Recent applications of KN1D
Comparisons against 2D codes
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 16
Currently trying to validate KN1D against 2D DEGAS2 simulations on DIII-D
New workflow uses experimental neutral measurements to constrain DEGAS2 simulations on DIII-D
Pratt et al. Nuclear Fusion (2026)
KN1D
OMP: good agreement (factor of ~2). Would agreement be improved with higher DEGAS2 mesh resolution?
FSA: lots of neutrals coming from the X-point in the DEGAS2 simulations, not captured by KN1D outer midplane geometry
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 17
Work is also ongoing to validate KN1D against C-Mod SOLPS/EIRINE simulations (D. Švorc)
kn1d-lite
M.A. Miller, PhD thesis (2025)
Preliminary results show faster decay of neutrals in kn1d-lite than in EIRENE
Still to check:
  Match rate coefficients + collisions
  Energy of the incident neutral beam in kn1d-lite
SOLPS simulations from:
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 18
Open Questions & Comments
Are there any standard test cases with fixed geometry, collisional processes and rate coefficients?
KN1D, SOLPS and DEGAS2 use three different sets of rate coefficients. Is there any consensus on what the most accurate rate coefficients are?
2D effects are clearly very important for the neutrals: is it possible to get away with a suitable 1D model for the purposes of reduced pedestal models?
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 19
Thank you!
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 20
Benchmarking
Some benchmarking was done on the charge-exchange terms between the original IDL KN1D and DEGAS2 in a slab geometry.
J.W. Hughes, PhD thesis (2005)
Good agreement was obtained but only after matching the CX rate coefficients in DEGAS2
Are there any standard test cases that can be used to benchmark these codes in a more systematic way?
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 21
How do KN1D results change when you add in elastic collisions?
DEGAS2 is run without elastic collisions. Elastic collisions on vs off does have a small effect on the KN1D results
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 22
How do KN1D and kn1d-lite profiles compare to the Saarelma-Connor neutrals model?
kn1d-lite with elastic scattering actually overpredicts slightly the DEGAS2 result – still lower than the Saarelma-Connor profile
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 23
How is the KN1D geometry chosen for DIII-D?
X_wall: use limiter position at the outer midplane (black solid line)
X_lim: the innermost flux surface that intersects both the upper and lower baffle: ‘window-frame’ method
Whyte et. al., PPCF (2005)
Lc: trace the contour of this innermost flux surface between the upper and lower baffles (in reality, results are not sensitive to this input)
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 24
How sensitive are KN1D results to spatial mesh resolution and velocity mesh resolution?
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC

## Slide 25
How do kn1d-lite results depend on the energy of the incident neutral beam at the separatrix?
Notes: Regular validation just uses Thomson scattering
But internally the model has to have a neutral density profile and an estimate for the diffusion strength in the pedestal. Can we validate these. YES! Ly-alpha. Signpost really clearly here. Next slide
Inform improvements to the model. I’ll give some ideas.
Apply to SPARC