## Slide 1: The kinetic neutral model in MHD code JOREK
ECW2026
Daniël Maris
S.Q. Korving, D.C. van Vugt , G. Su, M. Szűcs, A. Cathey, Y.C. Liang, E. Carrà, E. Waagaard, M. Hölzl, S. Wiesen, F.J. Artola, the JOREK team
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.

## Slide 2: Motivation
Do we really need another exhaust code?

## Slide 3: The dream exhaust code
Kinetic neutrals (like EIRENE)
Self consistent turbulence (like Grillix)
Dynamics on s timescale (like SOLPS-ITER recently)
Self consistent MHD (like JOREK)
Multi-fluid (like Hermes-3)
Unstructured grid (like wide grid SOLPS-ITER)
3D capability (like SOLEdge3X)
Stellarator capability (like EMC3-EIRENE)
Computational speed (e.g. GPU) (like Hermes-3)
…
✔*
✖*
✔
✔
✖*
✔*
✔
✔*
✔*
*it's more complicated
Wouldn't it be nice if … ?
that doesn’t exist

## Slide 4: Where JOREK shines: MHD interaction and dynamics
MHD
Self consistent ELMs & burn-through
ELM surpressed regimes
Disruptions and mitigation
Dynamics
Both plasma and neutrals fully time-dependent
Optimized, so s timescale tractable
There’s more to JOREK…
 Talk will focus on SOL applications
RMP effects on W transport
M. Hoelzl et al. NF 2026
2-way coupled full-f REs M. Hoelzl et al. NF 2026
Transient heat loads from SPI M. Hoelzl et al. NF 2026
Gyrokinetic NT/PT M. Bécoulet et al. PPCF 2026

## Slide 5: Current state
JOREK’s kinetic neutral model

## Slide 6: Meet
MHD: Euler equations + Maxwell +
  Magnetic potential (relates to B):
  Momentum:
  Density:
  Pressure:
Reduced MHD: restrict
Fully implicit: solve matrix system to find the change in the variables
MPI/OpenMP parallelized
Flux aligned iso-parametric G1 continuous finite elements
Fourier harmonics in toroidal direction
M. Hoelzl et al. NF 2021
JOREK, a massively parallel fully implicit non-linear extended magneto hydro dynamics (MHD) code
HELLO
my name is

## Slide 7: History of (neutral) kinetics
2015-2019: Daan van Vugt
Study W impurity transport/production during ELMs
Built first version of kinetics in library style
2019-2023: Sven Korving
Continue W impurity transport/production
For sputtering need reasonable target plasma
Made kinetic neutral model
2023-2024: Sharp increase in kinetic user/developers
"In those days, chaos ruled the land. Everyone did what was right in their own executable on their own branch, and there were no regression tests."

## Slide 8: Flexible particle framework
“Our great leader sent our hero, George, on a quest"
Flexibly combine particle species:
  Neutrals
  Impurities
  Runaway electrons
  Fast particles (e.g. NBI, alpha particles)
Single executable, on main branch, in main model
Object oriented control from input file
  Species, initialization, #particles, physics flags
Regression tests, wiki section
George Su et al.
Selection of input file:
! Deuterium neutral (D01)
part_group_configs(1)%coupling_scheme = 'ncs’
part_group_configs(1)%n_particles = 1d7
part_group_configs(1)%use_kin_ionisation = .t.
part_group_configs(1)%wall_act_configs(1)%type="reflection"
fluid_configs(1)%Z=-2
fluid_configs(1)%wall_act_configs(1)%type="wall recomb"
fluid_configs(1)%wall_act_configs(1)%target_group_id="D01"
fluid_configs(1)%wall_act_configs(1)%supers_weight_wall=1.d12
! Nitrogen impurities (N01)
part_group_configs(2)%coupling_scheme = 'ics'
part_group_configs(2)%n_particles = 1e6
part_group_configs(2)%use_kin_radiation = .t.
part_group_configs(2)%wall_act_configs(1)%type=“pump"
part_group_configs(2)%wall_act_configs(1)%weight_factor=0.7d0
part_group_configs(2)%puff_ctrl(1)%times = 0 1
part_group_configs(2)%puff_ctrl(1)%rates = 1.d21 1.d22
part_group_configs(2)%puff_ctrl(1)%supers_num_puff = 1000

## Slide 9: The kinetic neutral model
Array of Monte Carlo particles
  Position x, velocity v, weight w
  Particles typically live many fluid steps
Missing physics:
  molecular interactions
Simulation time: ~0.1s/day (AUG) on ~100CPUs
MPI/OpenMP parallelized
Slide: 5
Creation
Create particles:
Wall recombination (/sputtering)
Volumetric recombination
Puffing
Sources/sinks enter RHS of equations:
Momentum:
Density:
Pressure:
Solve
Sources/sinks projected to FE grid
Smoothing to reduce MC noise
For each particle timestep
For each particle
Push particle forward (update x)
Interpolate fluid quantities (at x)
Resolve ionization & CX (update v, w)
Inner loop
Proj.
Fluid
Kinetic particles
Resolve reflection & pumping (/sputtering)
Do neutral collisions

## Slide 10: Parallelization
Every MPI rank has own particle array
No spatial ownership of particles
Calculations are OpenMP multithreaded
Rank 1
Rank 2
Rank 3
Cubic Bezier Finite Elements
D. van Vugt PhD Thesis 2019

## Slide 11: Efficient particle feedback projection
Usual FE weak form
JOREK
Projected quantity
Test function
Shaping function
Feedback from i-th particle
Smoothing
Hyper-smoothing
w/
w/ and
No smoothing
Factorize once (think
Collapses to sum
Shaping function
D. van Vugt PhD Thesis 2019

## Slide 12: Current state
Recent work on kinetic neutral model

## Slide 13: 2T model implemented
MHD option: Evolve , instead of
Now added: Kinetic side compatible
Neutral energy to MHD:
For two-temperature model:
Máté Szűcs,
Sven Korving

## Slide 14: Neutral self collisions - algorithm
Distribute particles into collisional cells
Pair up randomly (!)
Determine collision chance
Collide
Unlike BGK (EIRENE):
Conserves energy to machine accuracy
Cross-section model: variable hard sphere
Does not assume Maxwellian
Collision
Before
After
Collisional cell
Daniël Maris

## Slide 15: Neutral self collisions - correctly captures diffusion:

## Slide 16: Intermediate timescales framework
Creation
Create particles:
Wall recombination (/sputtering)
Volumetric recombination
Puffing
Sources/sinks enter RHS of equations:
Momentum:
Density:
Pressure:
Solve
Sources/sinks projected to FE grid
Smoothing to reduce MC noise
Proj.
Fluid
Kinetic particles
==============================================
Starting inner particle loop
==============================================
sim%time : 0.17036211345290475
tstep_fluid_si : 1.1855071080336503E-005
aim tstep_particles : 4.9999999999999998E-007
used tstep_part_adj : 4.9396129501402099E-007
nstep_inner_loop : 24
lcm, n_lcm_blocks : 4 6
gcd, inner_stepsize : 2 2
Inner loop
Fluid timestep
Particle timestep
Intermediate timescale:
  Neutral collisions
  Particles that left domain:  Pumping, reflection, sputtering, later: association
From input: set integer particle steps
Backend: synchronizes everything (gcd & lcm)
Daniël Maris
For each particle timestep
For each particle
Push particle forward (update x)
Interpolate fluid quantities (at x)
Resolve ionization & CX (update v, w)
Resolve reflection & pumping (/sputtering)
Do neutral collisions

## Slide 17: GPU acceleration – initial approach
JOREK is Fortran, so bad GPU support
OpenMP offloading: no code duplication
Runaway electron evolution only
4x speedup on production testcase
Edoardo Carrà
P. Rác et al PASC ’26 2026

## Slide 18: GPU acceleration – new design
OpenMP offloading limitations:
  Limited hardware control
  Compiler-dependent performance and maturity
Recent studies demonstrated up to 32× speedup (M. Arrigo) using HIP
 developing JGX (JOREK GPU Acceleration) library:
  Fortran–C++ interoperability layer
  GPU-framework independent
  No code duplication
  Work for RE and FP
Edoardo Carrà

## Slide 19: Stellarator compatibility
Exhaust problem is unsolved challenge for future stellarators
Requires: neutrals, impurities, drifts and MHD in 3D stellarator geometry
Existing codes (e.g. EMC3-Eirene) do not couple all these
JOREK has stellarator plasma model
JOREK 3D with Fourier harmonics, so discrete divertor difficult
Kinetics is being prepared:
Kinetic – fluid coupling for stellarators
  Kinetics are reasonably model agnostic
  Source terms in stellarator model now implemented
  Ongoing testing
Sheath boundary conditions implemented for stellarators (next slide)
Elias Waagaard

## Slide 20
Stellarator compatibility
Sheath BC works
Artificial divertor indent in W7-A stellarator grid  sharper angles
Parallel velocity correct, particle + heat fluxes conserved
Next step: test more complex geometries like W7-X
JOREK – simulated
Expected from
Elias Waagaard

## Slide 21: Current state
Issues

## Slide 22: Issues: particle balance
Neutral particles lost due to bugs
 Fixed
Mismatch wall recombination calculation
Fluid side: effect of BC
Particle side: calculate
Calculation fixed for 1T
Calculation WIP for 2T (BC dependent)

## Slide 23: Issues: stability
Flickering momentum source
Implicit plasma, explicit neutrals
Particles see last plasma timestep
Accumulated drag > local momentum
Experience/solutions?
Idea: forward extrapolation of fields
Negative plasma density
Idea: implicit density source
Momentum source to plasma
Flickering
Momentum source (a.u.)

## Slide 24: Results
Overview of code use

## Slide 25: Overview of code use

## Slide 26: ITER PFPO-1 simulations – Sven Korving
Gas puff scan in (ITER PFPO-1 H-mode 1.8T/5MA/20MW)
  SOLPS-ITER (J.-S. Park NF 2021)
    Eirene ( neutrals), , without drifts
  JOREK
    Kinetic atoms
JOREK detaches at higher
  No molecules, n-n collisions, dome channel
   Less momentum/energy losses
S. Korving et al. PoP 2023
Drifts cause stronger inner-outer asymmetry and stronger decrease of power to wall
  Strong transition coincides with formation HFSHD-region
Notes: Ask Sven Korving: transition he means 2.25e19?

## Slide 27: HFSHD-region formation in ITER
ExB drifts + neutrals drives formation
  HFSHD-region is driven by ExB vortex
  Redirection ion and heat flow
  Accumulates & mixes cold and hot plasma
  Stronger energy dissipation around vortex
Affects poloidal flow in the entire SOL
Sven Korving
Ionisation rate
Neutral density
ExB flow
Electron density
S. Korving et al. PoP 2023

## Slide 28: Small-ELM burn-through
Re-attachment (as experiments)
Nitrogen flush-out (as experiments)
Máté Szűcs
Peak divertor temperatures

## Slide 29: XPR formation in ASDEX Upgrade
MHD + kinetic D neutrals & N impurities
Yu-Chih Liang
Stable XPR formation
Impurity radiation
Poloidally localised XPR (as exp.)
Impurity radiation
Neoclassical impurity collisions
Y. C. Liang et al. PoP 2026

## Slide 30: XPR transitions; loss and MARFE
Decrease N seeding rate
XPR moves downward
Impurity radiation decays
Loss of XPR (as experiments)
Yu-Chih Liang
Increase N seeding rate
XPR moves upward
Te in XPR reduces to << 1 eV
MARFE formation (as experiments)
Impurity radiation
Electron temperature
Y. C. Liang et al. PoP 2026

## Slide 31: XPR quantitative validation AUG
Máté Szűcs
Prad
Te
ne
Notes: synthetic diagnostics

## Slide 32: QCE access in ASDEX Upgrade
QCE regime is a type-I ELM-free H-mode in AUG
AUG #36165: type-I ELMy to QCE regime
Transition follows from gas puff ramp
Kinetic neutrals at various puffing rates in JOREK simulations result in a transition from type-I ELMs to quasi-continuous pedestal instabilities
  Low gas puff (purple) results in type-I ELM onset
  Increasing gas puff shows quasi-continuous transport of instabilities (which are borne near the separatrix)
Andrés Cathey
AUG #36165 gas puff ramp (top) and ELM monitor (bottom). Type-I ELMs give way to QCE regime as the separatrix density increases with stronger puffing.

## Slide 33: Detachment dynamics – proof of concept
Goal my PhD: Numerical system identification for ITER
Proof of concept results:
ITER SRO phase
Promising but missing molecules, validation
Daniël Maris
Input: puff rate
Model
Output:

## Slide 34: Detachment dynamics validation attempt: Quantitative mismatch
WPTE RT05, AUG #42651, collab F. Cursi
Attached -> detached dynamically
Dynamic simulation 0.17s
Mismatch: too attached, pipe dynamics
Plasma temperature
Plasma density

## Slide 35: Detachment dynamics validation: Qualitative agreement
Experiment:
Fast up, slow down of experiment radiation peak
XPR like
Simulation:
Fast up (60ms), slow down of T & D0 density
XPR like
Plasma temperature
Ionization
Radiation peak in experiment
Simulation
Ionization (a.u.)

## Slide 36: Final words
Conclusion and outlook

## Slide 37: Conclusion: JOREK shines
Thanks!
MHD
ELMs, surpression & burn-through
Dynamics
Fully time-dependent and optimized
Maturing fast
Flexible framework
Parallelized
Efficient feedback
2T, NNC, timescales
JOREK is open source, so do try at home!
Outlook
Develop JGX, stellarators
Sheath BC for current
Molecules
Ionization (a.u.)