## Slide 1
J Omotani, F Parra, M Barnes, S Newton, M Hardman, M Abazorius, L McConnell
Kinetics for Transport (KfT)
1D1V demo of moment-kinetic approach to transport

## Slide 2: Overview
Aim : consistent transport timescale simulation of open and closed field line regions
Issues :
Strong parameter variation on open lines - issue for grid resolution
Moment-kinetic approach :
Define shape function with known constant velocity moments
Solve consistent shape function evolution equation coupled to moment equations
Implementation :
Numerical framework Kinetics for Transport (KfT) : [https://github.com/KineticsforTransport/KfT]
Finite element (Chebyshev, Legendre), written in
[https://julialang.org]
Sheath boundary effect
Momentum conservation
coupled through electrostatic potential - drifts affect divertor loading
}

## Slide 3: Moment-kinetic approach - 1D1V
Kinetic equation for a charged species
Define shape function :
- shifted to local parallel flow frame
Transport equations :
- usual velocity moments of interest
- normalised to satisfy fixed constraints on density, parallel momentum, energy

## Slide 4: Moment-kinetic approach - 1D1V
Kinetic equation for a charged species
Define shape function :
- shifted to local parallel flow frame
- marginalised in 1D1V
Transport equations :
- usual velocity moments of interest
- normalised to satisfy fixed constraints on density, parallel momentum, energy

## Slide 5: Moment-kinetic approach - 1D1V
Consistent (marginalised) shape function evolution equation
modified collision and source terms
- contain all marginalised contributions from
moment substitution [slide 15]
note for grid spacing

## Slide 6: Moment-kinetic approach - electrons
Consistent (marginalised) shape function evolution equation
On ion dynamic timescales, light electrons → - electron distribution pseudo-steady-state
- neglect terms consistently : flow comparable to , ion collisions with electrons …
note for grid spacing

## Slide 7: Implementation - KfT - grid
Finite element framework : Zero out negative values of shape function
Chebyshev or Legendre polynomial basis supported
- here all Chebyshev, [Legendre: Hardman et al Comp Phys Comm 314 109675 (2025)]
- derivatives : first order - matrix method via Lagrange polynomials, *also FFT for Chebyshev (fast for high-order)
second order - weak method representation (LU factorization with UMFPACK)
- interpolation : w grids eg for cross-species coupling: Chebyshev FFT, Legendre project via Lagrange basis
- integration : Clenshaw-Curtis quadrature with weights precomputed by FFT for Chebyshev
Gaussian quadrature with weights calculated by FastGaussQuadrature.jl for Legendre
- non-uniform grid spacing : compressed near walls to capture strong variations, eg in electrostatic potential
- element boundaries set at distance from wall proportional to square of grid index
- non-uniform spacing in velocity : due to term in advection, parallel velocity grid compensates
~ uniform inside threshold, coarser at large with element size
Parallelisation : hybrid distributed and shared memory scheme
- ‘MPI+MPI’ implementation, avoids openMPI thread overhead
- only spatial grid domain-decomposed here
* gotcha : apply method just as in Boyd reduces order

## Slide 8: Implementation - KfT - BCs
Ions : don’t return from wall
- sets condition
- if steady state falls near grid point, evolving solution could have discontinuous jumps
→ cap grid point value to prevent oscillation
Recycling neutrals : return ion flux as marginalised Knudsen distribution
at set wall temperature Tw
Moment constraints : at end of each RK stage, shape function won’t generally satisfy the constraints
- apply correction so does : [slide 17]
Kinetic electrons : determine one-sided tail cutoff vcut to set current into wall - here taken insulating
- electrons below vcut reflected, iterate vcut evaluation and constraint equations
Initialisation : warm Maxwellian (~ source T), modified to enforce wall BCs, moment constraints applied

## Slide 9: Implementation - KfT - time-advance
Explicit and semi-implicit time advance methods available
Generic RK methods with fixed or adaptive timestep
- cap at factor of CFL on grid
- error is mean over all independent variables, so not dominated by many points of shape function
To reach transport timescales kinetic electrons must be treated implicitly
- electron shape function strongly coupled to electron energy (parallel pressure) evolution equation
- use as preconditioner
→ use IMplicitEXplicit Additive RK scheme
- other species, cross-field transport …. treated explicitly
- retain artificial time dependence in pseudo steady-state electron shape equation
- 2 methods working : pseudo-transient continuation or retain explicit time-derivative (no other small mass term)

## Slide 10: Implementation - KfT - IMEX ARK JFNK
Solve implicit part of system with preconditioned JFNK iteration
- weighted norm includes relative tolerance, not just absolute, to act properly on tails where values are small
- preconditioner uses lagged Jacobian method
- periodically evaluate full J, serial LU factorised
- [ongoing] parallellisation of preconditioner for 2D2V - layout of and
- ‘soft’ forcing of electron moment constraints
during Krylov iteration by adding :
- electron boundary condition re-applied at end of each Newton iteration
Moment constraints fully enforced at end of each RK+implicit stage
IMplicitEXplicit Additive RK scheme

## Slide 11: Example : adiabatic electrons
Light electrons → simplify electron response :
- replace electrostatic potential in ion equations directly, only ion kinetic equation to solve, explicit
Upstream source of particles
& energy T=300eV, Te=100eV
Lz=±10m
Krook self-collisions
z : ngrid=6, nel=N-1
w|| : ngrid=5, nel=2N
N = 32,64,128,256
- res test final timestep 10-8
Infinite potential gradient expected near the wall
[Ewart et al PPCF 64 015010 (2022)]
- effect captured with increasing resolution
- check kinetic Bohm condition
[Harrison & Thompson
Proc Phys Soc 74 145 (1959)]
n
T||
u||
-0.3
0.3
0.0
0.6
1.0
0.6
1.0
-0.3
0.3
0.0
-0.3
0.3
0.0
1
-1
0
z
N
128
256
64
32
RBohm
1.0
2.0

## Slide 12: Example : …. convergence
Ion distribution function, N=256
white : contour 10-i, i=1…16
Edges of map are edges of w|| grid
v = ui|| ±vti Lw||
orange : ui||
Final moment constraint correction value (A-1)
- B,C similar
z

## Slide 13: Example : …. convergence
Ion distribution function, N=256
white : contour 10-i, i=1…16
Edges of map are edges of w|| grid
v = ui|| ±vti Lw||
orange : ui||
Infinite gradients near wall
→ nonstandard convergence analysis
- RMS error decreases ~ Nel-2
- compressed z-grid → size element at wall ~ Nel-2
→ ? global accuracy linear in smallest element
- max error small
→ accuracy of dynamics away from sheath
much higher than global error estimate

## Slide 14: Example : …. + recycling neutrals
Add kinetic neutral population recycling from target : same 1D equations without in momentum equation
- midplane source 200eV, Te=20eV, wall temperature Tw=10eV in Knudsen distribution, recycling coefficient 0.5
- ionisation and charge-exchange collision operators - used constant cross-sections, no neutral self-collisions
Periodic boundary conditions : implementation benchmark with decay of damped modes [Excalibur report link]
- deflation method used to find multiple solutions [Farrell et al SIAM J Sci Comput 37
A2026 (2015)]
fn
fi
midplane source 200eV, Te=20eV
z : compressed near target
ngrid=9, nel=32
w|| : uniform
ngrid=10, nel=63

## Slide 15: Ongoing and future work
Papers in prep
1D1V - KfT framework, implementation and examples
1D1V - effect of collisionality, sources and convergence to collisional limit [McConnell et al, Sherwood`25]
1D2V - effect of field strength variation [McConnell et al, Sherwood`26, EPS`26]
Stability analysis of helical drift kinetic system with sheath [Parra et al, APS`25, Sherwood`26, Varenna`26]
2D2V solver
- MPI parallelisation of preconditioner
- benchmark loss rate in mirror geometry with model collisions
- benchmark to full-f solver
- cold ion demo of electric field formation in 2D geometry with open and closed field lines
Multi-ions
- complete implementation
- test model collision operators, explore cost of coupling to full Fokker-Planck collision operator
…. turbulence equations in development
JTO : gotchas

## Slide 16: Example : kinetic ions and electrons
Repeat pure plasma test with midplane source - T=300eV for both species, N=32 (low res but tight threshold)
- timestep ~ adiabatic case – 3.6ns (ke) vs 14.4ns (ae), ~ 10’s Krylov iterations per RK stage
- serial run time ~ 100x higher/output step → optimize iteration counts + preconditioner
JTO : gotchas and issues in development of 2D parallelization
- mobile electrons couple whole grid → direct matrix solve - exploit “small” structured grid vs typical literature
- static condensation exploiting sparsity structure (grid points only couple in elements)
- bespoke parallelism treating layout of and
~ 75% complete : shared memory structure working, distributed MPI to finish + plumbing
n
u||
-0.3
0.3
0.0
0.5
1.0
0.75
1.25
-0.3
0.3
0.0
-0.3
0.3
0.0
1
-1
0
z
kinetic
adiabatic

## Slide 17: Details ….

## Slide 18: 1D1V system - definitions
Modified sources collect all collision and source terms,
Write in terms of the marginalized contributions

## Slide 19: Implementation details
Spatial grid : element boundaries
Velocity grid : element boundaries transition smoothly around Tcoarse from uniform to
Midplane source - marginalised form
Non-uniform grid

## Slide 20: Implementation - moment constraints
At the end of each RK stage, the current shape function won’t generally satisfy the constraints
- define the applied correction so that does :
- 3x3 matrix inverse for A,B,C :
Modification to prevent oscillation at sheath entrance going towards steady state
- weight so B,C corrections go to 0 at :