## Slide 1
Hermes-3 performance and neutral model update
M. Kryjak, B.D. Dudson, M. R. Hardman, C. MacMackin, H. Al Daas, N. Bootland, M. Tsagkaridis, S. Mijin, W. Saunders, J. Cook and J. Buchanan
Tokamak Energy project collaborators: M. Moscheni, L. Balbinot, J. Bryant, M. Romanelli
+ Hermes-3 collaborators, the rest of the VANTAGE team, and the international community

## Slide 2: This talk
Hermes-3 performance journey
Brief kinetic neutral update

## Slide 3: Hermes-3
  Developed for 3D/1D: Originally an evolution of SD1D/Hermes-2/STORM
  Focus of our work is 2D: catching up with SOLPS
Feature | Status
Language / portability / parallelism | C++ / GPU port in progress / MPI
Dimensions / time dependence | 1D, 2D, 3D steady and unsteady/time dependent
Numerical scheme | Fully implicit Newton-Krylov
Preconditioners | Physical and algebraic (LU/ILU)
Discretisation scheme | Conservative finite difference (like FV)
Discretisation order | Second order with slope limiters and Lax flux
Coordinate scheme | Fully field aligned or Flux Coordinate Independent (FCI)
Notes: Intro to Hermes-3, recycle from old PPTs

## Slide 4: First Hermes-3 verification in 2D
Part of ongoing collaboration with Tokamak Energy (M. Moscheni, L. Balbinot, J. Bryant, M. Romanelli)
Hermes-3 fluid neutrals vs. SOLPS/SOLEDGE2D with EIRENE
Low fidelity: no currents, impurities, drifts
New Hermes-3 features:
Fast/thermal reflection, recycling
Decay length BC
Recycling at radial boundaries
Separate flux limiters for neutral diffusion, conduction, viscosity
Hermes-3
SOLPS-ITER
SOLEDGE2D
See L. Shih’s poster from earlier today for physics investigation

## Slide 5: First Hermes-3 verification in 2D
Part of ongoing collaboration with Tokamak Energy (M. Moscheni, L. Balbinot, J. Bryant, M. Romanelli)
Hermes-3 fluid neutrals vs. SOLPS/SOLEDGE2D with EIRENE
Low fidelity: no currents, impurities, drifts
New Hermes-3 features:
Fast/thermal reflection, recycling
Decay length BC
Recycling at radial boundaries
Separate neutral flux limiters for diffusion, conduction, viscosity
Hermes-3
SOLPS-ITER
SOLEDGE2D
This caused extreme performance degradation!

## Slide 6: The performance journey…
Tests from scratch, 0-100ms, flat initialisation, 10 cores (MPI)

## Slide 7: The performance journey…
Tests from scratch, 0-100ms, flat initialisation, 10 cores (MPI)
●
measured
◐
extrapolated
Full-resolution ST40
40x100 grid, flux limiter = 0.2
~600
hrs
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 8: The performance journey…
Many causes investigated:
Flooring/positivity issues
Operator bugs
Solver settings
Grid quality
Obscure numerical modes
Boundary conditions
All hit a roadblock until recent months!
●
measured
◐
extrapolated
~600
hrs
Tests from scratch, 0-100ms, flat initialisation, 10 cores (MPI)
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 9: Testing at low resolution is more tractable
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
Low-resolution ST40
20x50 grid, flux limiter = 1.0
~600
hrs
~82
hrs
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 10: First breakthrough: full algebraic preconditioning using PETSc
Scheme: Backward Euler
Preconditioning: LU (MUMPS)
Timestep: adaptive
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
~60
hrs
1
hr
Collaboration with:
STFC team: H. Al Daas, A. Pillai, A. Sunderland, J. Castagna
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 11: Reducing non-differentiability
#1 Neutral perp flux limiter: improve regularisation
More robust
Prevents a lot of crashes
More accurate than previous approach
Similar or faster performance
#2: Slope limiter: switch to differentiable form
More robust, faster
Significant reduction in solver failures
More consistent, robust performance
Low-res ST40, flux limit α = 0.2–1.0, from scratch to 123.5 ms, one run per point. Scans: appendix.
Slope limiters make advection more upwind when gradients change fast
Switch to Van Albada slope limiter:
Fully differentiable
More diffusive
Monotonised Central (MC)
Van Albada 1 (VA)
master
no regularisation
this work
Kink
Kink
Issues when denominator or
Improved regularisation:
Smooth floor, ceiling
Smooth abs()
Notes: - Brief intro to slope limiters
Show why MC is non-differentiable and how Van Albada is
Scan comparison showing MC vs VA on shipped default regularisation – both physics results, wall time and wall time variability

## Slide 12: Reducing non-differentiability
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
41
hrs
40
min

## Slide 13: Column scaling and limiter lagging
#3: PETSc SNES solver
Column (variable) scaling
~20x speedup
ST40 to 100 ms (C. MacMackin, poster)
~20x speedup
Speedup reduced when solver optimised
Left: low-res ST40 state at 100 ms. Right: low-res ST40, α = 0.2–1.0, solver without variable scaling, to 123.5 ms.
#4: Neutral perp flux limiter:
Lag evaluation of
Periodically renormalise matrix passed to solver:
Freeze gradient in denominator during linear/nonlinear iterations
after scaling
unlagged
lagged
with ,
and
Notes: Here we introduce the scale_vars work (SNES-MUMPS-3) and show that it can lead to significant speedups, but also say how it can lead to lagging causing issues
Note that this is C. MacMackin’s work

## Slide 14: Column scaling and limiter lagging
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
42
min
63
sec
Note: lagging and column scaling are not commutative – with a highly tuned solver, lagging can reduce performance.

## Slide 15: Can we optimise solver settings with AI?
Developed during a hackathon with
Problem
Idea
“Best” solver settings are a moving target
Black-box optimisation techniques not good at teaching
SNES solver has 865 parameters:
binary
237
discrete
371
continuous
223
string
34
Semi-autonomous exploration
re-run as the code changes
Intelligent search
With human help (initially)
Interpretable, durable knowledge
Make lots of reports and talk to them
Solver tuning is tedious
Notes: Philosophy of AI use: must be interpretable, I must learn to be a numerics expert, use it for exploration and then we do development/code use ourselves, etc.
Application: Hermes-solver-opt. Make simple flowchart to show how it works.
Slide must communicate that we are using AI responsibly and not as a black box, and that these are explorations to build on.
It must also show how much work we’ve put into all the skills, rules, guards, durable knowledge formats, beads etc.
Assume audience don’t know much about AI and may not trust it.
Include bit about hackathon trip to Google/google deepmind with their logo.

## Slide 16: Agentic solver tuning framework
Developed during a hackathon with
researcher
1 Study plan
2 Performance tests
3 Physics / performance check
4 Report
AI
AI
AI
AI
agent
researcher
adversarial agents
iterate until reasonable plan, use findings to improve framework
0.1 ms
1 ms
100 ms
Many cheap short runs,
then full 0–100 ms run
✓
✗
Make sure steady-state answer unchanged
AI
AI
AI
AI
agent
researcher
adversarial agents
Iterate until all is clear, use findings to improve framework
next study
The framework
Instructions
3 files, 63 rules
General agent behaviour control
Skills
10 skills, 1,550 lines
How to run, analyse, report
Guards
Runs, builds, overnight work
Rules enforced by deterministic scripts
Knowledge store
1,169 runs
33 claims
215 tasks
Deterministic
Deterministic
Notes: Philosophy of AI use: must be interpretable, I must learn to be a numerics expert, use it for exploration and then we do development/code use ourselves, etc.
Application: Hermes-solver-opt. Make simple flowchart to show how it works.
Slide must communicate that we are using AI responsibly and not as a black box, and that these are explorations to build on.
It must also show how much work we’ve put into all the skills, rules, guards, durable knowledge formats, beads etc.
Assume audience don’t know much about AI and may not trust it.
Include bit about hackathon trip to Google/google deepmind with their logo.

## Slide 17: Example results of an overnight study (~700 runs)
1 ms
2.9x speedup across 5 repeats
Rung 0 (~0.1ms)
Rung 1 (1ms)
Rung 2 (100ms)
Notes: Results of solver-opt S03, the wall time plot with the three rungs

## Slide 18: Solver tuning impact
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
16
min
99
sec

## Slide 19: MAST-U performance gets worse!
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
■
MAST-U, 20x100, flux limiter = 1.0
16
min
99
sec
36
hrs
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 20: Can an agentic workflow investigate MAST-U performance?
1 Study plan
2 Edit code
3 Run & analyse
4 Report
AI
AI
AI
AI
agent
researcher
adversarial agents
iterate until plan is reasonable
AI
AI
AI
AI
agent
researcher
adversarial agents
iterate until all is clear
upstream
own branch
no push
Local clone
Pushing disabled
run
analyse
overnight, inside
agreed bounds
next study
Same framework
instructions
skills
guards
knowledge store
Pull request
Humans:
Use AI code as example
Implement separately
Notes: This is now a flowchart of how the dev campaigns work

## Slide 21: Overnight investigation
● ion density
● ion pressure
Where failed solves start, 0–1 ms
● ion momentum
● neutral momentum
● other equations
New solver failure diagnostics found failure hotspot: OMP
Pressure and density gradients extremely flat
Notes: Problem: MAST-U is very slow
This is due to solver failures, so we investigated what caused them
Please show figure of failure locations from the test5-failures report as well as the gradients at midplane
Please mention what diagnostics were already available for this and what diagnostics were added
Say how the issue was isolated to the ion momentum equation in low gradient regions

## Slide 22: Solution found: slope limiter tolerance
[1] G. D. van Albada, B. van Leer and W. W. Roberts, Astron. Astrophys. 108, 76–84 (1982), eq. 37
Van Albada et al. (1982) [1]:
with ε: central difference
van Albada (as run)
Slope limiter reconstruction chatter
Cell differences much smaller than Newton step -> noise leading to reconstruction chatter
Solution: smoothly disable limiter for small differences

## Slide 23: Results
Huge speedup!
Answer unchanged
Baseline: ~36 h
Slope limiter fix: 121 s (!!)
Notes: Background: ST40 is now very fast, but MAST-U is still extremely slow
First serious test of autonomous Hermes-3 optimisation/development workflow (test5-failures)
Found that the Van Albada limiter was implemented without a crucial term from the original paper, causing a large sensitivity in flat gradients
Performance results: extreme speedup on MAST-U

## Slide 24: Impact of slope limiter tolerance
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
■
MAST-U, 20x100, flux limiter = 1.0
17
min
85
sec
121
sec

## Slide 25: In appendix: Jacobian pattern optimisation
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
■
MAST-U, 20x100, flux limiter = 1.0
10
min
54
sec
70
sec
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 26: Finally, trying separate limiters again…
●
measured
◐
extrapolated
●
ST40, 40x100, flux limiter = 0.2
▲
ST40, 20x50, flux limiter = 1.0
■
MAST-U, 20x100, flux limiter = 1.0
64
sec
72
sec
10
min
Performance solved apart from ST40 high resolution – see appendix.
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 27: Overall speedup summary
Tests from scratch, 0-100ms, from flat profiles
~680× faster
~115 h
10 min
all fixes, combined limiters
CVODE-1, combined limiters
~4,700× faster
~82 h
1 min
all fixes, separate limiters
CVODE-1, separate limiters
700× faster
14 h
1 min
all fixes, separate limiters
CVODE-1, separate limiters
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 28: Caveats
These cases are:
  Low fidelity (one main ion, no currents, no drifts)
  Small machines (MAST-U, ST40)
Performance gains not always transferable
  Most in this talk are not applicable to 3D turbulence
  More testing is required – different conditions, machines
Status: all PRs on Hermes-3 Github apart from slope limiter tolerance and Jacobian colouring pattern optimisation
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 29: Conclusions
Fully implicit codes can be very sensitive to discontinuities
When those are resolved, fully implicit codes can be very fast
With experience from the performance project and help from agentic workflows, issues can be resolved at an accelerated pace
Notes: This is a hero slide: full run test 4 and test 5 performance, counting all improvements chronologically. We need:
CVODE-1 with combined limiters
CVODE-1 with separate limiters (unregularized)
SNES-MUMPS-1 with separate limiters
SNES-MUMPS-1 with separate limiters, regularisation
+ Van Albada
+ lagging of the limiter gradient
+ SNES-MUMPS-3
+ Jacobian colouring optimisation
+ Van Albada tolerance (Test5-failures)
For the slowest cases like the earliest ones, we may have to estimate due to time constraints. This needs to be one big plot filling the entire slide. Y axis will be discrete and describe each change, newest/fastest at the top. X axis will be continuous and give average time to 100ms plasma time from scratch.

## Slide 30
Hermes-3 – VANTAGE coupling

## Slide 31: Introduction to VANTAGE
Kinetic neutral framework built on NESO-Particles
PIC/DSMC style particle scheme
Modern, scalable, GPU-native, performance-portable codebase
Key features already available:
  Atomic reactions
  Reflection and recycling/sources
  TRIM processes
  BGK collision models
  Particle population management
event-splitting and advection
event products/details
Notes: Bits from Stefan’s talk
Benefits against EIRENE: performance-portable, DSMC capability, flexibility
Disadvantages: inherently less performant scheme for steady-state
Current capabilities

## Slide 32: Initial implementation plan
Initial objective: explicit coupling in 2D only
Hermes-3 and VANTAGE are both C++: linked and compiled together
    No need for separate interface
Anticipating to spend a lot of time on optimisation:
    Load balancing
    Linearisation schemes
Plasma iteration
Plasma iteration
Linearised sources
Plasma
Neutrals
Plasma iteration
Linearised sources
Kinetic neutrals
Kinetic neutrals
Particle substeps
Particle substeps
⋮
Notes: - Initial coupling scheme: explicit with linearisation
- Flowchart showing implementation plan and status

## Slide 33: Current status
Coupled IZ/REC balance test (density channel)
Coupled IZ/REC balance test (all channels)
Field-aligned slab recycling test
Tokamak test (no vessel)
Higher fidelity tokamak test
Milestone test plan
Triangular neutral grid
Particle advection in vessel grid
Density coupled
slab IZ/REC equilibration test

## Slide 34: Thank you - Questions
Fluid neutrals
Performance
Kinetic neutrals
Impurities
Drifts
Molecules (O. Parry, Wed 14:16)
Verification/validation on MAST-U (L. Shih, Wed 14:24)
VANTAGE coupling
(this talk)
JET neon-seeded baseline (new hire in 2027)
Work at LLNL (M. Tsagkaridis, B. Dudson Fri 09:40)
Zhdanov implemented this FY (C. MacMackin)
Verification/validation on ST-40 (this talk)
Solver optimisation in collab. with STFC (This talk, C. MacMackin, Thu 14:24)
Physical preconditioning for neutrals (N. Bootland, Thu 14:12)
Stellarator drifts simulations (T. Tork Tue 16:20)
GPU porting (J. Castagna, Thu 10:00)
VANTAGE-Reactions
(S. Mijin, Wed 13:40)
Verification/validation for stellarators (A. Stier, Thu 14:16)
Summary of Hermes-3 projects:

## Slide 35
Appendix

## Slide 36: Lesson #1: regularise neutral limiter without changing physics
non-differentiable kink due to
saturated limiter turns diffusion into advection, operator is central
!
!
!
Make absolute smooth
Add smooth ceiling
Make floor smooth
Improvement
Peak outer target
Average speed
did not finish
●
Old code
◆
No regularisation
■
This work
●
Old code
◆
No regularisation
■
This work
More robust, similar performance
Regularisation affects answer less
Notes: One slide to present the optimise-neutral-fluxlim work but before van albada.
Maths to show why regularisation is needed:
When limiter saturated, diffusion becomes advective
Blow up to infinity at shallow gradients
Non-smooth abs()
Then performance results – the scan with no regularisation, scan with master, then scan with shipped default normalisation. both physics results, wall time and wall time variability

## Slide 37: Lesson #2: lagging nonlinear terms
sets both the flux and its limit, so is strongly nonlinear
!
Improvement
Freeze during Newton and linear steps
Neutral cross-field diffusive flux
: regularised
Peak outer target
Average speed
◆
Unlagged
■
Lagged
◆
Unlagged
■
Lagged
Lagging 8–51× faster
Same answer, within 0.1%
Notes: Talk about why the gradient makes the limiter so nonlinear, and how lagging works.
Show results of lagging vs no lagging with separate limiters on floor 10.
Lagging gradient only.

## Slide 38: Lesson #3: slope limiter kinks
!
MC, previous default
φ(r) plots: Wikipedia, "Flux limiter", by Griffgruff, CC BY-SA 3.0, cropped. Grey: second-order TVD region.
Slope limiters: operators that dynamically change reconstruction order to improve robustness (similar to SOLPS hybrid scheme)
Non-differentiable kink
Van Albada: smooth curve, no corners
Improvement
Peak outer target
Average speed
■
MC (shipped defaults)
●
Van Albada
■
MC (shipped defaults)
●
Van Albada
More robust, faster performance
Very little impact on answer
Notes: - Brief intro to slope limiters
Show why MC is non-differentiable and how Van Albada is
Scan comparison showing MC vs VA on shipped default regularisation – both physics results, wall time and wall time variability

## Slide 39: Fix 4: Jacobian colouring optimisation
13 cells
assumed for
every field pair
11 cells
neutral density eqn,
electron pressure
5 cells
ion density eqn,
ion momentum
1 cell
ion momentum eqn,
neutral pressure
RHS evaluations per Jacobian build
RHS evaluations per full run
Two runs each; end states within 0.1 %; 261 of 637 cells kept
Finite differences: one RHS evaluation per column
Columns that never share a row are perturbed together: one per colour
Fewer couplings → fewer colours → cheaper Jacobian
Full ST40 full res test run, 0–100 ms: 16 min → 9.5 min, 1.7× faster, same answer
Notes: Brief intro to Jacobian colouring
Figure of new, calculated pairs, and the bar chart showing reduction in RHS evaluations
Single number of performance improvement

## Slide 40: Extending to separate limiters
Separate limiters now a smaller slowdown
Performance penalty remains
Likely due to added nonlinearity
Average speed
[ms simulated / 24 h wall]
Peak outer target [eV]
◆
Separate, minimal reg.
■
Separate, shipped reg.
●
Combined
▲
Separate, no regularisation
DATA STATUS No-regularisation arm
✓ flux limits 1.0, 0.5, 0.2 (splim20d, 20ea, 20f)
✗ flux limits 0.4, 0.8: prepared (splim20k, 20j), not queued
? 0.2 point: checkerboarding check open (fl-88d)
Notes: How the regularisation for parallel is scaled off perpendicular
How the viscosity regularisation is derived from the rest with vn_bar
Then scan comparison of separate limiters with little regularisation, then shipped regularisaton, and combined limiters. Same slides as the previous scan comparisons

## Slide 41: Separate limiters: a runaway to a hot SOL
Separate
Combined
Cross-field conduction limited
outer divertor legs, far SOL: ½ of combined
Heat trapped
in outer divertor legs
Neutrals hotter, thinner
at the same pressure
Less ionisation
0.7× by 30 ms
SOL starved
fewer particles
SOL hotter
sheath-limited
Hot SOL, 580 eV: solver stalls
!
feeds back
steep gradient in outer divertor legs
Dashed: possible link, untested
Flux limit 0.2 unless stated; gradient floor 10 /m, ceiling 100 /m
Separatrix , outer midplane
■
Combined, all limits 0.2
■
Separate, all limits 0.2
■
Separate, conduction limits 0.1
■
Separate, ⊥ conduction limiter off

## Slide 42: Appendix: why the limiter is so nonlinear
Sketch: floor and ceiling off (); a single cell, whereas in the model each cell's also depends on its neighbours.
start
answer
one Newton step
Lagging: freeze at the start of each timestep, in every limiter. Then is linear in : no convergence radius, and Newton is exact for this term in one step.
The gradient sets both the flux and its limit:
Saturation is large wherever the neutrals are collisionless (: mean free path).
  Newton's slope falls as : at it is 1/121 of the unlimited slope
  Newton converges only within about of a sign change. From towards , one step lands at , the wrong sign, and the iteration diverges

## Slide 43: Separating flux limiters